## Slide 1: NVL Ax RVP strategy
NVL RVP Architecture
Deepak, Mayank, Ranganadh, Manju, Sachin, Mani
WW15p5Y2025
Rev0.50

## Slide 2: RVP SKU Strategy History
WW26p1 : RVP Rev0p0.5 - SKU Strategy for NVL Ax PC
WW08p1’2025: Rev0p0.55 - Ax02- HSIO SKU dropped post alignment with NVL Ax FV team, integration of AM SKU requirements on same RVP.
WW15p5’2025: Rev0p0.70 - Added Risk and Open towards EC

## Slide 3: NVL AX/AM RVP Strategy
NVL AX/AM RVP SKU Strategy
Opens:
100WcTDP PL1 support on RVP - Bigger HS will impact KOZ around CPU
Risk: 125W TDP PL1 support on RVP [ECG] - Bigger HS will impact KOZ around CPU and may impact RVP SKU strategy [ VR design change, PCB change etc], PD and thermal data awaited
Check Point – WW24 for 125W data, impact analysis to RVP post reception of power numbers.
Memory Validation plan with MOP
Minimum EV specific topologies (min/ max/ re driver less etc) Support [ request to leverage NVL-HX EV data] , yet to finalize w.r.t. RVP floorplan, can potentially affect RVP IO mapping.
NVL Ax T3 Socketed RVP
PDG + Primary SKU
NVL Ax T3 Socketed HSIO RVP*
This SKU is TBD
HSIO/EV/SI/PI/PPV -WIP
Golden BKC, PnP
EV/SI/PI, GFx, PPV , ECG(IOTG)
Ax 01
Ax 02
RVP strategy assumptions
Only T3 RVP SKU
Discrete only PD Solution.
Ax 02 SKU is placeholder only - Dropped
Single RVP to support Both AX & AM Silicon. No Over clocking support.
PCH IOE support is motherboard down with support limited to HSIO for SSD
RVP BOM sku will be considered to support w/o PCH IOE Config
HSIO FV/EV Support: No FV specific AIC support, ask to leverage data from NVL Hx RVP. – Alignment done with HSIO FV team, no separate HSIO RVP to be supported.
Silicon/ Package info
Segment | CPU | GPU & NPU | PL1 Range | Memory
AX/AM | 8+16+4/4+8+4 | 512EU/256EU & NPU7 - 6Tile | 35W-60W-70W | LP5x MD @ 10.7 GT/s- MOP
DROPPED

## Slide 4: NVL Ax/Am RVP BOM SKU's
Segment | Base Board# | RVP SKU | Base board SKU/ BOM SKU | RVP SKU Code | RVP Base board SKU + BOM SKU (Please note - SKU name will change later with MySamples Tool name) | Validation Config | SoC Support | PCH IOE Support (Mother Board Socketed) | PCB Type (POR L# + RVP L#)
Ax | Ax/Am 01 RVP | NVL Ax/Am LP5x MOP T3 with PCH IOE RVP | Base Board SKU | Ax-011 | NVL Ax/Am LP5x MOP T3 | Volume runner | NVL Ax/Am SoC | With Out PCH IOE | Type-3, 10L+6L
 |  |  | BOM SKU | Ax-012 | NVL Ax/Am LP5x MOP T3 | PnP SKU |  | With Out PCH IOE | 
 |  |  | PPV Board SKU | Ax-013 | NVL Ax/Am LP5x MOP T3 with PCH IOE PPV RVP | PPV |  | TBD | 
 |  |  | BOM SKU | Ax-014 | NVL Ax/Am LP5x MOP T3 with PCH IOE RVP |  |  | With PCH IOE | 
 |  |  | BOM SKU | Ax-015 | NVL Ax/Am LP5x MOP T3 with PCH IOE RVP | ECG |  | With PCH IOE | 
 |  |  | BOM SKU | Ax-016 | NVL Ax/Am LP5x MOP T3 | Memory DV |  | TBD | 
 |  |  | BOM SKU (Placeholder) | Ax-017 | AM Specific (PI Changes) BOM SKU- TBD |  |  | TBD | 

## Slide 5: Opens: To be closed by RVP Team
Socket Design Strategy Closure
VR Controller finalization and enabling

## Slide 6: Tentative Schedule:

## Slide 7: SOCKET Mechanical Design Challenges
Temperature range: The thermal solution needs to be redefined. We need to find out the required temperature validation range.
Wattage: the package is much bigger than LNL. It will be a socket design challenge.
DV, EV and FV validation requirements. It depends on each discipline's needs; multiple memory interposers need to be designed. The RVP KOZ also needs to be defined.
Memory socket design: The horseshoe like memory placement is on the package..
Priolo, Matthew G

## Slide 8: Memory Socket Scheme for RVP
Socket Development for RVP : Initial plan to scale LNL solution to NVL Ax.
ACK: Atkins, Aviva

## Slide 9: Memory Socket Scheme for RVP
ACK: Atkins, Aviva

## Slide 12: New RVP Requirements for OSAT Testing
Ask: Cost efficient smaller FF RVP to increase testing throughput at OSAT
Data Awaited:
  Board Size versus throughput O/P- From OSAT Vendor: Need data to understand correlation between board size versus testing throughput at OSAT
  Testing samples per week requirements at OSAT- From ATTD
Propose Solution:
  If throughput is not a concern: Optimized RVP BOM SKU with debug hooks, connectors and not required interfaces circuitry unpopulated
  If throughput is concern:
    New RVP with smaller FF, less layer count and limited interfaces support for memory testing requirements : New RVP to be added and designed.
    Two Board RVP approach: Main board: POR interfaces and limited debug hooks, Secondary board: Noncritical debug hooks. Avoid any new RVP Spin. To be intercepted in given RVP.