## Slide 1: NVL S RVP Update
NVL RVP Architecture
System PDT
Yuan, Simon; Lai, Kenneth; Liu, Yuan Erh; Prakash, Lakshmi; U, Vinay
WW23Y2025
Rev1.60
NVL RVP PDT sharepoint

## Slide 2: RVP SKU Strategy History
WW18p5Y2024: RVP Rev1p08 - Rearranged NVL-S RVP SKU code #
WW22p4Y2024: RVP Rev1p09 - Desktop, Hx & UPH strategy slides, assumptions and opens merged and other minor updates, boot kit & AIC list slides added to S and Hx segment
WW25p3Y2024: RVP Rev1p1 - Separated Desktop RVP SKU strategy from main PPT
WW36p1Y2024: RVP Rev1p3 - Updated Type-C topology
WW01p5Y2025: RVP Rev1p5
  Updated S-061 HSIO PCB stackup
  CCB to intercept TBT-USB4 Retimer POR simplification, HSD link - https://hsdes.intel.com/resource/15017235143
  CCB to change Front-panel Type-C solution, ZBB’ed FFC implementation - https://hsdes.intel.com/resource/13012628919
WW03p3Y2025: RVP Rev1p51
  Updated S-061 HSIO TCSS Type-C configuration using M.2 TCSS Module AIC
WW04p1Y2025: RVP Rev1p52
  Updated S-061 HSIO TCSS Type-C configuration using Rood Bridge soldered down
WW23p1Y2025: RVP Rev1p6
  DDR5 4R cUDIMM module topology intercepted in S01x / S02x (internal validation) and S051 (UDIMM 1DPC 6L, POR)
    CCB https://hsdes.intel.com/appstore/article-one/#/article/14024323700
  S031 TCSS port config updated as per CCB, TCP1 with M.2 TCSS module AIC with max routing length (internal PoC), components unstuffed by defaults. TCP0 default config is Type-C retimerless topology (Rework option to enable M.2 TCSS module AIC)
    CCB https://hsdes.intel.com/appstore/article-one/#/article/13012604833, TBT Front-panel Type-C proposal ZBB’ed

## Slide 3
Silicon/ Package info
RVP strategy and assumptions
All RVP support ATX-like FF (except HSIO SKU).
uATX design will be soft collateral. SODIMM 2DPC will be Whitepaper. CAMM not POR for S segment and no RVP SKU planned.
SKU S011 / S012 / S021 / S022 are base-board and BOM SKUs based on DDR5 UDIMM 1DPC BOB reference design. S011 (PnP) / S 012 (PPV) are capable of validating PL1=PL2 with addition of VR heatsink. S021 (CRB) is Golden config SKU and volume runner. S022 is BOM SKU for CPV.
TBT-USB4 retimer POR implementation and validation as per CCB intercept
M.2 TCSS module supported on S01x, S02x, S031 and S041, multiple versions of M.2 TCSS module AIC can be validated on those RVP SKUs. S051 and S061 to implement TBT retimer solder-down solution as PDG requirements.
Detailed information can be found in NVL PDT sharepoint
DDR5 4R cUDIMM topology supported on S01x, S02x and S051
RZL-S/TTL-S platform to reuse the NVL-S RVP boards as planned.
NVL-S RVP SKU Strategy
NVL S DDR5 UDIMM 1DPC T3 4L (10L) RVP
PDG + Primary SKU
Golden BKC, PnP, Multi-Rail PSU
EV, FV, SIV, GFx, CPV, PPV
NVL S DDR5 UDIMM 2DPC T3 6L (10L) RVP
PDG SKU – dTBT support
Delta BKC, PnP, ATX12VO
EV, FV, SIV, GFx
NVL S DDR5 UDIMM 1 DPC OC T3 6L (12L) RVP
PDG SKU – Overclocking (XMP)
Delta BKC, Partial PnP, Multi-Rail PSU
EV, FV, SIV, GFx
NVL S DDR5 SODIMM 1DPC T3 6L (10L) RVP
PDG SKU – dTBT support
NVL S HSIO T3 (12L) RVP
HSIO SKU, UDIMM 1DPC 4L
PCD/PCH PCIe PHY, Multi-Rail PSU
Delta BKC, PnP, ATX12VO
EV, FV, SIV, GFx
FV, EV, HSIO validation
S 031
S 041
S 051
Segment | CPU | GPU & NPU | PL1 Range | Memory | PCB Type
S | 4+0+4 4+8+4 8+16+4 8+16+4 (bLLC) 2x (8+16)+4 | 32EU & NPU6 4Tile | 35-65W 35-150W 125-250W | cUDIMM/cSODIMM 1DPC @8000MT/s | Type-3
 |  |  |  | cUDIMM 2DPC @5600MT/s | Type-3
 |  |  |  | OC UDIMM 1DPC (XMP) @up to 16GT/s-G4 | Type-3
S 061
NVL-S RVP SKU Strategy
S 011
S 012
S 021
S 022
WW23Y2025
Notes: Need support from 3PE to update sample schedule for USB4 80G redriver / DP2.1 retimer / HDMI2.1 retimer & redriver

## Slide 4: NVL Desktop RVP SKU Summary
N-1 ERB
SKU Code # | Segment | RVP SKU Name | Base board SKU/ BOM SKU | RVP Base board SKU + BOM SKU (Will change with MySamples Tool SKU name later) | Memory Support | PCB Type | PSU | Validation Config | Type-C / Display Config | 2x7 PnP HDR | Power Accumulator Config (PAC1954)
S-011 | S | NVL-S DDR5 UDIMM 1DPC | Base Board SKU | S-011: NVL-S DDR5 UDIMM 1DPC EV w/ PnP HDR | cUDIMM 1DPC 8000 2R (up to 128GB) (4R cUDIMM) | Type 3 4L + 8L | Multi-rail | Full PnP HDR, PL1=PL2 w/ Validation and Debug hooks | 2x BP TCSS M.2 module 2x DP2.1 FsDP connector | Yes | PnP/System Meter(Default) *Energy Telemetry(Optional)
S-012 |  |  | BOM SKU | S-012: NVL-S DDR5 UDIMM 1DPC PPV |  |  |  | PPV, PL1=PL2 |  | No (Unstuffed) | PnP/System Meter for CPU rails only
S-021 |  |  | Base Board SKU | S-021: NVL-S DDR5 UDIMM 1DPC CRB w/o PnP HDR |  | Type 3 4L + 6L |  | Volume Runner w/o Validation and Debug hooks | 2x BP TCSS M.2 module 1x DP2.1 FsDP connector 1x HDMI2.1 connector | No (Unstuffed) | Energy Telemetry(Default) *PnP/System Meter(Optional)
S-022 |  |  | Board SKU | S-022: NVL-S DDR5 UDIMM 1DPC CPV |  |  |  | CPV |  | No (Unstuffed) | PnP/System Meter for PCH rails only
S-031 | S | NVL-S DDR5 UDIMM 2DPC | Base Board SKU | S-031: NVL-S DDR5 UDIMM 2DPC | cUDIMM 2DPC 5600 2R/2R (up to 256GB) | Type 3 6L + 4L | Single-rail | Delta config Full PnP HDR supported | TCP0 BP Type-C retimerless (rework to TCSS M.2 module) TCP1 Type-C with TCSS M.2 Module AIC (unstuffed by default, internal PoC) | Yes | PnP/System Meter(Default) *Energy Telemetry(Optional)
S-041 | S | NVL-S DDR5 SODIMM 1DPC | Base Board SKU | S-041: NVL-S DDR5 SODIMM 1DPC | cSODIMM 1DPC 8000 2R (up to 128GB) | Type 3 6L + 4L | Single-rail | Delta config Full PnP HDR supported | 2x BP TCSS M.2 module | Yes | Energy Telemetry(Default) *PnP/System Meter(Optional)
S-051 | S | NVL-S DDR5 UDIMM 1DPC OC | Base Board SKU | S-051: NVL-S DDR5 UDIMM 1DPC OC | cUDIMM 1DPC XMP speed (up to 128GB) (4R cUDIMM) | Type 3 6L + 6L | Multi-rail | Delta config, Overclocking Partial PnP HDR supported | 2 x BP TBT retimer onboard with 80G routing | Yes, without VCCIA support | PnP/System Meter(Default) *Energy Telemetry(Optional)
S-061 | S | NVL-S HSIO UDIMM 1DPC | Base Board SKU | S-061: NVL-S HSIO UDIMM 1DPC | cUDIMM 1DPC | Type 3 4L + 8L | Multi-rail | HSIO Validation Full PnP HDR supported | 2 x BP TBT retimer onboard with 40G routing | Yes | No support
WW23Y2025

## Slide 5: NVL-S RVP – M.2 TCSS Module
Feature Support | S011 / S012 NVL S DDR5 UDIMM 1DPC | S021 / S022 NVL S DDR5 UDIMM 1DPC | S031 NVL S DDR5 UDIMM 2DPC | S041 NVL S DDR5 SODIMM 1DPC | S051 NVL S DDR5 UDIMM 1DPC OC | S061 NVL S HSIO UDIMM 1DPC
SKU Code | EV/PnP & PPV | Golden Config EV/CRB & CPV | Delta SKU | Delta SKU | Delta SKU | HSIO (PCIe bifurcation)
Pkg name: TYPEC_[0] TC1 (USB4 / HDMI2.1 / DP 2.1 ) | Back Panel TCSS Module (Default RBR module) 1) Rood Bridge w/ integrated PD, w/ EC I3C (707) 2) June Bridge w/ discrete PD (TI PD) , w/ EC I3C (109) 3) DP 2.1 UHBR20 retimer w/ sDP connector (400) 4) HDMI 2.1 12G retimer (302) 5) Type-A repeaterless (redriverless) (600) | Back Panel TCSS Module (Default RBR module) 1) Rood Bridge w/ integrated PD, w/ EC I3C (707) 2) June Bridge w/ discrete PD (TI PD) , w/ EC I3C (109) 3) DP 2.1 UHBR20 retimer w/ sDP connector (400) 4) HDMI 2.1 12G retimer (302) 5) Type-A repeaterless (redriverless) (600) | Default config: Vertical Type-C retimerless w/ Discrete PD solder-down Rework option: Back Panel TCSS Module (Default RBR module) 1) Rood Bridge w/ integrated PD, w/ EC I3C (707) 2) June Bridge w/ discrete PD (TI PD) , w/ EC I3C(109) | Back Panel TCSS Module (Default RBR module) 1) Rood Bridge w/ integrated PD, w/ EC I3C (707) 2) June Bridge w/ discrete PD (TI PD) , w/ EC I3C (109) 3) DP 2.1 UHBR20 retimer w/ sDP connector (400) 4) HDMI 2.1 12G retimer (302) 5) Type-A repeaterless (redriverless) (600) | Back Panel Type-C TBT retimer soldered down w/ EC I3C TCP0/TCP1 shared SPI Flash | Back Panel Type-C TBT retimer soldered down w/ EC I3C TCP0/TCP1 shared SPI Flash
Pkg name: TYPEC_[1] TC2 (USB4 / HDMI2.1 / DP 2.1 ) | Back Panel TCSS Module (Default RBR module) 1) Rood Bridge w/ integrated PD (707) 2) June Bridge w/ discrete PD (TI PD) (109) 3) DP 2.1 UHBR20 retimer w/ sDP connector (400) 4) HDMI 2.1 12G retimer (302) | Back Panel TCSS Module (Default RBR module) 1) Rood Bridge w/ integrated PD (707) 2) June Bridge w/ discrete PD (TI PD) (109) 3) DP 2.1 UHBR20 retimer w/ sDP connector (400) 4) HDMI 2.1 12G retimer (302) | TCSS Module (Components unstuffed, rework option, internal PoC) 1) Rood Bridge w/ integrated PD 2) June Bridge w/ discrete PD (TI PD) 40G long routing (Internal PoC validation) | Back Panel TCSS Module (Default RBR module) 1) Rood Bridge w/ integrated PD (707) 2) June Bridge w/ discrete PD (TI PD) (109) 3) DP 2.1 UHBR20 retimer w/ sDP connector (400) 4) HDMI 2.1 12G retimer (302) | Back Panel Type-C TBT retimer soldered down TCP0/TCP1 shared SPI Flash | Back Panel Type-C TBT retimer soldered down TCP0/TCP1 shared SPI Flash
1x Barlow Ridge dTBT AIC | N/A | N/A | 1x dTBT Barlow Ridge AIC @PCH PCIe x4 CEM slot #2 | 1x dTBT Barlow Ridge AIC @ PCD-S PCIe x4 CEM slot #3 | N/A | N/A
 | M.2 TCSS Module Support List | M.2 TCSS Module Support List | M.2 TCSS Module Support List | M.2 TCSS Module Support List | M.2 TCSS Module Support List | M.2 TCSS Module Support List
 | 1. M.2 TCSS Module (Card 707) - Rood Bridge single retimer (5V/3A) * Rood Bridge with integrated PD 2. M.2 TCSS Module (Card 109) - June Bridge single retimer (5V/3A) * June Bridge with discrete PD (TI PD) 3. M.2 TCSS Module (Card 400) - DP2.1 retimer (enhanced sDP connector) 4. M.2 TCSS Module (Card 302) - HDMI 2.1 retimer 5. M.2 TCSS Module (Card 600) - Type-A redriverless / repeaterless 6. M.2 TCSS Module (Card 702) - Gothic Bridge single retimer (5V/3A) * Gothic Bridge with integrated PD, Not POR, internal validation only | 1. M.2 TCSS Module (Card 707) - Rood Bridge single retimer (5V/3A) * Rood Bridge with integrated PD 2. M.2 TCSS Module (Card 109) - June Bridge single retimer (5V/3A) * June Bridge with discrete PD (TI PD) 3. M.2 TCSS Module (Card 400) - DP2.1 retimer (enhanced sDP connector) 4. M.2 TCSS Module (Card 302) - HDMI 2.1 retimer 5. M.2 TCSS Module (Card 600) - Type-A redriverless / repeaterless 6. M.2 TCSS Module (Card 702) - Gothic Bridge single retimer (5V/3A) * Gothic Bridge with integrated PD, Not POR, internal validation only | 1. M.2 TCSS Module (Card 707) - Rood Bridge single retimer (5V/3A) * Rood Bridge with integrated PD 2. M.2 TCSS Module (Card 109) - June Bridge single retimer (5V/3A) * June Bridge with discrete PD (TI PD) 6. M.2 TCSS Module (Card 702) - Gothic Bridge single retimer (5V/3A) * Gothic Bridge with integrated PD, Not POR, internal validation only 7. M.2 TCSS Module (Card 70x) - Rood Bridge single retimer (5V/3A), Front-panel Type-C with 10" internal Type-C cable (Feasibility WIP) | 1. M.2 TCSS Module (Card 707) - Rood Bridge single retimer (5V/3A) * Rood Bridge with integrated PD 2. M.2 TCSS Module (Card 109) - June Bridge single retimer (5V/3A) * June Bridge with discrete PD (TI PD) 3. M.2 TCSS Module (Card 400) - DP2.1 retimer (enhanced sDP connector) 4. M.2 TCSS Module (Card 302) - HDMI 2.1 retimer 5. M.2 TCSS Module (Card 600) - Type-A redriverless / repeaterless 6. M.2 TCSS Module (Card 702) - Gothic Bridge single retimer (5V/3A) * Gothic Bridge with integrated PD, Not POR, internal validation only | N/A | N/A
NVL PDT Links:
NVL-S RVP LZ
NVL-S RVP HAS
WW23Y2025

## Slide 6: Back up

## Slide 7: NVL Desktop RVP SKU Summary
WW04Y2025
N-1 ERB
SKU Code # | Segment | RVP SKU Name | Base board SKU/ BOM SKU | RVP Base board SKU + BOM SKU (Will change with MySamples Tool SKU name later) | Memory Support | PCB Type | PSU | Validation Config | Type-C / Display Config | 2x7 PnP HDR | Power Accumulator Config (PAC1954)
S-011 | S | NVL-S DDR5 UDIMM 1DPC | Base Board SKU | S-011: NVL-S DDR5 UDIMM 1DPC EV w/ PnP HDR | UDIMM 1DPC 8000 2R (up to 128GB) | Type 3 4L + 8L | Multi-rail | Full PnP HDR, PL1=PL2 w/ Validation and Debug hooks | 2x BP TCSS M.2 module 2x DP2.1 FsDP connector | Yes | PnP/System Meter(Default) *Energy Telemetry(Optional)
S-012 |  |  | BOM SKU | S-012: NVL-S DDR5 UDIMM 1DPC PPV |  |  |  | PPV only, PL1=PL2 |  | No (Unstuffed) | PnP/System Meter for CPU rails only
S-021 |  |  | Base Board SKU | S-021: NVL-S DDR5 UDIMM 1DPC CRB w/o PnP HDR |  | Type 3 4L + 6L |  | Volume Runner EV/SI/PI w/o Validation and Debug hooks | 2x BP TCSS M.2 module 1x DP2.1 FsDP connector 1x HDMI2.1 connector | No (Unstuffed) | Energy Telemetry(Default) *PnP/System Meter(Optional)
S-022 |  |  | Board SKU | S-022: NVL-S DDR5 UDIMM 1DPC CPV |  |  |  | CPV only |  | No (Unstuffed) | PnP/System Meter for PCH rails only
S-031 | S | NVL-S DDR5 UDIMM 2DPC | Base Board SKU | S-031: NVL-S DDR5 UDIMM 2DPC | UDIMM 2DPC 5600 2R/2R (up to 256GB) | Type 3 6L + 4L | Single-rail | Delta config Full PnP HDR supported | 1x BP TCSS M.2 module (rework to Type-C retimerless) 1x FP Type-C with TCSS M.2 Module AIC | Yes | PnP/System Meter(Default) *Energy Telemetry(Optional)
S-041 | S | NVL-S DDR5 SODIMM 1DPC | Base Board SKU | S-041: NVL-S DDR5 SODIMM 1DPC | SODIMM 1DPC 8000 2R (up to 128GB) | Type 3 6L + 4L | Single-rail | Delta config Full PnP HDR supported | 2x BP TCSS M.2 module | Yes | Energy Telemetry(Default) *PnP/System Meter(Optional)
S-051 | S | NVL-S DDR5 UDIMM 1DPC OC | Base Board SKU | S-051: NVL-S DDR5 UDIMM 1DPC OC | UDIMM 1DPC XMP speed (up to 128GB) | Type 3 6L + 6L | Multi-rail | Delta config, Overclocking Partial PnP HDR supported | 2 x BP Rood Bridge onboard with 80G routing | Yes, without VCCIA support | PnP/System Meter(Default) *Energy Telemetry(Optional)
S-061 | S | NVL-S HSIO UDIMM 1DPC | Base Board SKU | S-061: NVL-S HSIO UDIMM 1DPC | UDIMM 1DPC | Type 3 4L + 8L | Multi-rail | iVE/FV HSIO Validation Full PnP HDR supported | 2 x BP Rood Bridge onboard with 40G routing | Yes | No support

## Slide 8: NVL Desktop RVP SKU Summary
SKU Code # | Segment | RVP SKU Name | Base board SKU/ BOM SKU | RVP Base board SKU + BOM SKU (Will change with MySamples Tool SKU name later) | Memory Support | PCB Type | PSU | Validation Config | Type-C / Display Config | 2x7 PnP HDR | Power Accumulator Config (PAC1954)
S-011 | S | NVL-S DDR5 UDIMM 1DPC | Base Board SKU | S-011: NVL-S DDR5 UDIMM 1DPC EV w/ PnP HDR | UDIMM 1DPC 8000 2R (up to 128GB) | Type 3 4L + 8L | Multi-rail | PnP HDR, PL1=PL2 w/ Validation and Debug hooks | 2x BP TCSS M.2 module 2x DP2.1 FsDP connector | Yes | PnP/System Meter (Default) *Energy Telemetry (Optional)
S-012 |  |  | BOM SKU | S-012: NVL-S DDR5 UDIMM 1DPC PPV |  |  |  | PPV only, PL1=PL2 |  | No (Unstuffed) | PnP/System Meter for CPU rails only
S-021 |  |  | Base Board SKU | S-021: NVL-S DDR5 UDIMM 1DPC CRB w/o PnP HDR |  | Type 3 4L + 6L |  | Golden Config, EV/SI/PI w/o Validation and Debug hooks | 2x BP TCSS M.2 module 1x DP2.1 FsDP connector 1x HDMI2.1 connector | No (Unstuffed) | Energy Telemetry (Default) *PnP/System Meter (Optional)
S-022 |  |  | Board SKU | S-022: NVL-S DDR5 UDIMM 1DPC CPV |  |  |  | CPV only |  | No (Unstuffed) | PnP/System Meter for PCH rails only
S-031 | S | NVL-S DDR5 UDIMM 2DPC | Base Board SKU | S-031: NVL-S DDR5 UDIMM 2DPC | UDIMM 2DPC 5600 2R/2R (up to 256GB) | Type 3 6L + 4L | Single-rail | Delta config Full PnP HDR supported | 1x BP TCSS M.2 module (rework to Type-C retimerless) 1x FP Type-C with TCSS M.2 Module AIC | Yes | PnP/System Meter (Default) *Energy Telemetry (Optional)
S-041 | S | NVL-S DDR5 SODIMM 1DPC | Base Board SKU | S-041: NVL-S DDR5 SODIMM 1DPC | SODIMM 1DPC 8000 2R (up to 128GB) | Type 3 6L + 4L | Single-rail | Delta config Full PnP HDR supported | 2x BP TCSS M.2 module | Yes | Energy Telemetry (Default) *PnP/System Meter(Optional)
S-051 | S | NVL-S DDR5 UDIMM 1DPC OC | Base Board SKU | S-051: NVL-S DDR5 UDIMM 1DPC OC | UDIMM 1DPC XMP speed (up to 128GB) | Type 3 6L + 6L | Multi-rail | Delta config, Overclocking Partial PnP HDR supported | 2 x BP Rood Bridge onboard with 80G routing | Yes, without VCCIA support | PnP/System Meter (Default) *Energy Telemetry (Optional)
S-061 | S | NVL-S HSIO UDIMM 1DPC | Base Board SKU | S-061: NVL-S HSIO UDIMM 1DPC | UDIMM 1DPC | Type 3 4L + 8L | Multi-rail | iVE/FV HSIO Validation Partial PnP HDR supported | 2x BP TCSS M.2 module | Yes | No support
WW03Y2025