## Slide 1: WCL U RVP: LZ Response
WW48.2’23

## Slide 2: Supported by RVP
Power delivery: 15W
Audio: HD-A, SNDW, and I2S
WWAN: M.2 Key B socket, with GNSS <Part # TBD>
CNVi: M.2 Key E socket <GfP 2/4, WhP 2, SpP>
Discrete WLAN+BT: TyP2/Gale Peak via M.2 Key E socket
Display: Embeded: eDP, External: DP2.1 (only up to HBR 3 and thru TCSS IO only)/HDMI2.0b (Only thru Native DDI port, no TCSS IO support)
USB type-A and type-C (HBR, GBR, Third Party Redriver <Analogix, TI>, 2x Type A WUP, 1 x USB 3.2 Type A over TCSS IO)
GbE: Jacksonville (No Foxville support)
SPI NOR <1x64MB>, EC via eSPI, PCIe Gen 4 device
Type-3 PCB
UFS 3.1 Gear 4 thru LM AIC
PD controller: TBD
IMVP9.3 power delivery, 3S1P battery
I2C and SPI touch, scan matrix keyboard by EC, I2C touchpad, lid switch, power button, USB based FPS
Validation/debug: USB Dbc, MIPI60 merge JTAG and PCH VISA connector, SINAI2/NEVO, TTK3, DnX over USB2, dTPM, SD 7.0 via PCIe,
Integrated LP5x VR

## Slide 3: Not supported by RVP
DDR5 UDIMM and down, LPCAMM
Integrated 4G/5G modem/RF down
No Foxville support
No eMMC
No MIPI Display and Camera
HW mic disable- HW Yes, SW enabling open??
NFC
Type-4 PCB
ATX support
1S and 2S battery config
USB4 OTG
Elixir, Optane NVMe, Optane 2LM
BC1.2, CDP, and DCP for system charging
HDMI2.1 with LSPCON
No DP Connector on Native DDI
No HDMI on TCSS Ios
No PD AIC <PD Controller integrated on TCSS IO module>
No flash sharing for GBR/BBR Retimer
No Stylus Support
No TBT 20G Supported

## Slide 4: Open
5G M.2 module interception
Clarity on RFI/EMC testing on RVP
UCIe LDO or power option
Memory Part finalization
USB2.0 based Camera Part finalization
Closure on low-cost integrated battery charger
Closure on CEC and Energy Star compliance as applicable to RVP
Closure on PD controller part