## Slide 1: R-02 To Resolve VCCIO Boot-up Failure
NVL-S RVP
Required Rework Document

## Slide 2: R-02
Change Log | 2025 WW30
Description | This rework is to fine-tune the VCC sequence of the VCCIO VR
Impact | The V5A will follow V5DSW to turn on without MOSFET control. The total Power consumption will be higher(~2mW) during DSx.
Rework Involved | SMD resistor
SKUs | S-031 FAB1
Contacts | Chen, Ellen ; Wang, Ivan B
HSD Link | N/A
Collateral Link | N/A
SW Dependency | N/A
To Resolve VCCIO Boot-up Failure

## Slide 3: NVL-S RVP S-031 Top

## Slide 4: NVL-S RVP S-031
Action | REFDES | Description
STUFF | R873 | RES D,0402,1.00 kOHM,1.00%,1/16W
Step 1 of 1
TOP
R873

## Slide 5: NVL-S RVP S-031
Action | Item | REFDES | Current IPN | Description | New IPN | Description
STUFF | RESISTOR | R873 | NA | NA | A93548-023 | RES D,0402,1.00 kOHM,1.00%,1/16W
R-02 To Resolve VCCIO Boot-up Failure
Rework Summary