## Slide 1: S-01B To Disable JTAG ODT and Enable Onboard Terminations
NVL-S
Suggested Rework Document

## Slide 2: S-01B
Change Log | 2025 WW28.1 : Initialized 2025 WW28.3 : Adding S031 portion and modifying the title and description for clarity 2025 WW32.7 : Modifying the pull-up resistors for PREQ_N, PRDY_N, MBPB[0], MBPB[1] 2025 WW34.5 : Adding the delta note from S-01A to S-01B
Description | This is a rework to disable JTAG ODT and replace it with the onboard terminations to cover the A0 silicon bugs.
Impact | Without this rework, DBC/XDP won’t be able to function.
Rework Involved | SMD Resistors
SKUs | S01x/S02x/S031 RVP
Contacts | Lai, Kenneth ; Lin, Nick1 ; Liu, Yuan Erh
HSD Link | https://hsdes.intel.com/appstore/article-one/#/article/22021359138 https://hsdes.intel.com/appstore/article-one/#/article/22021359156
Collateral Link | N/A
SW Dependency | N/A
To Disable JTAG ODT and Enable Onboard Terminations

## Slide 3
Index
Board SKU | Index
S01x/S02x | Refer to p.4 ~ p.10
S031 | Refer to p.11 ~ p.17
Those boards with S-01A implemented already | Refer to p.18~p.30

## Slide 4
S01x/S02x

## Slide 5: S01x/S02x TOP

## Slide 6: S01x/S02x TOP

## Slide 7: S01x/S02x BOT

## Slide 8: S01x/S02x
Action | REFDES | Description
STUFF | R2B48 | RES D,0402,1.00 kOHM,1.00%,1/16W
STUFF | R3B52 | RES D,0402,51.00 OHM,5.00%,1/16W
STUFF | R2B45 | RES D,0402,100.00 OHM,1.00%,1/16W
REPLACE | R3B68 | RES D,0402,100.00 OHM,1.00%,1/16W
Step 1 of 2
TOP
R2B48
R2B45

## Slide 9
Step 2 of 2
BOT
Action | REFDES | Description
STUFF | R2M15 | RES D,0402,51.00 OHM,5.00%,1/16W
STUFF | R3M15 | RES D,0402,51.00 OHM,5.00%,1/16W
STUFF | R3M16 | RES D,0402,100.00 OHM,1.00%,1/16W
STUFF | R3M24 | RES D,0402,51.00 OHM,5.00%,1/16W
REPLACE | R2N7 | RES D,0402,100.00 OHM,1.00%,1/16W
R2M15
R2N7
R3M24
S01x/S02x

## Slide 10: NVL-S S01x/S02x
Action | Item | REFDES | Current IPN | Description | New IPN | Description
STUFF | Resistor | R2B48 | N/A | N/A | A93548-023 | RES D,0402,1.00 kOHM,1.00%,1/16W
STUFF | Resistor | R3B52 | N/A | N/A | A93549-007 | RES D,0402,51.00 OHM,5.00%,1/16W
STUFF | Resistor | R2B45 | N/A | N/A | A93548-043 | RES D,0402,100.00 OHM,1.00%,1/16W
REPLACE | Resistor | R3B68 | A93549-023 | RES D,0402,10.00 kOHM,5.00%,1/16W | A93548-043 | RES D,0402,100.00 OHM,1.00%,1/16W
STUFF | Resistor | R2M15 | N/A | N/A | A93549-007 | RES D,0402,51.00 OHM,5.00%,1/16W
STUFF | Resistor | R3M15 | N/A | N/A | A93549-007 | RES D,0402,51.00 OHM,5.00%,1/16W
STUFF | Resistor | R3M16 | N/A | N/A | A93548-043 | RES D,0402,100.00 OHM,1.00%,1/16W
STUFF | Resistor | R3M24 | N/A | N/A | A93549-007 | RES D,0402,51.00 OHM,5.00%,1/16W
REPLACE | Resistor | R2N7 | A93549-023 | RES D,0402,10.00 kOHM,5.00%,1/16W | A93548-043 | RES D,0402,100.00 OHM,1.00%,1/16W
S-01B To Disable JTAG ODT and Enable Onboard Terminations Rework Summary

## Slide 11
S031

## Slide 12: S031 TOP

## Slide 13: S031 TOP

## Slide 14: S031 BOT

## Slide 15: S031
Step 1 of 2
TOP
Action | REFDES | Description
STUFF | R2B48 | RES D,0402,1.00 kOHM,1.00%,1/16W
STUFF | R3B52 | RES D,0402,51.00 OHM,5.00%,1/16W
STUFF | R3M15 | RES D,0402,51.00 OHM,5.00%,1/16W
STUFF | R3M16 | RES D,0402,100.00 OHM,1.00%,1/16W
STUFF | R2B45 | RES D,0402,100.00 OHM,1.00%,1/16W
REPLACE | R3B68 | RES D,0402,100.00 OHM,1.00%,1/16W
R2B48
R3B68
R2B45

## Slide 16: S031
Step 2 of 2
BOT
Action | REFDES | Description
STUFF | R2M15 | RES D,0402,51.00 OHM,5.00%,1/16W
STUFF | R3M24 | RES D,0402,51.00 OHM,5.00%,1/16W
REPLACE | R2N7 | RES D,0402,100.00 OHM,1.00%,1/16W
R2M15
R2N7

## Slide 17: NVL-S S031
Action | Item | REFDES | Current IPN | Description | New IPN | Description
STUFF | Resistor | R2B48 | N/A | N/A | A93548-023 | RES D,0402,1.00 kOHM,1.00%,1/16W
STUFF | Resistor | R3B52 | N/A | N/A | A93549-007 | RES D,0402,51.00 OHM,5.00%,1/16W
STUFF | Resistor | R2B45 | N/A | N/A | A93548-043 | RES D,0402,100.00 OHM,1.00%,1/16W
REPLACE | Resistor | R3B68 | A93549-023 | RES D,0402,10.00 kOHM,5.00%,1/16W | A93548-043 | RES D,0402,100.00 OHM,1.00%,1/16W
STUFF | Resistor | R2M15 | N/A | N/A | A93549-007 | RES D,0402,51.00 OHM,5.00%,1/16W
STUFF | Resistor | R3M15 | N/A | N/A | A93549-007 | RES D,0402,51.00 OHM,5.00%,1/16W
STUFF | Resistor | R3M16 | N/A | N/A | A93548-043 | RES D,0402,100.00 OHM,1.00%,1/16W
STUFF | Resistor | R3M24 | N/A | N/A | A93549-007 | RES D,0402,51.00 OHM,5.00%,1/16W
REPLACE | Resistor | R2N7 | A93549-023 | RES D,0402,10.00 kOHM,5.00%,1/16W | A93548-043 | RES D,0402,100.00 OHM,1.00%,1/16W
S-01B To Disable JTAG ODT and Enable Onboard Terminations Rework Summary

## Slide 18
from S-01A to S-01B

## Slide 19
S01x/S02x

## Slide 20: S01x/S02x TOP

## Slide 21: S01x/S02x BOT

## Slide 22: S01x/S02x
Action | REFDES | Description
STUFF | R2B45 | RES D,0402,100.00 OHM,1.00%,1/16W
REPLACE | R3B68 | RES D,0402,100.00 OHM,1.00%,1/16W
Step 1 of 2
TOP
R2B45

## Slide 23
Step 2 of 2
BOT
Action | REFDES | Description
STUFF | R3M24 | RES D,0402,51.00 OHM,5.00%,1/16W
REPLACE | R2N7 | RES D,0402,100.00 OHM,1.00%,1/16W
R2N7
R3M24
S01x/S02x

## Slide 24: NVL-S S01x/S02x
Action | Item | REFDES | Current IPN | Description | New IPN | Description
STUFF | Resistor | R2B45 | N/A | N/A | A93548-043 | RES D,0402,100.00 OHM,1.00%,1/16W
REPLACE | Resistor | R3B68 | A93549-023 | RES D,0402,10.00 kOHM,5.00%,1/16W | A93548-043 | RES D,0402,100.00 OHM,1.00%,1/16W
STUFF | Resistor | R3M24 | N/A | N/A | A93549-007 | RES D,0402,51.00 OHM,5.00%,1/16W
REPLACE | Resistor | R2N7 | A93549-023 | RES D,0402,10.00 kOHM,5.00%,1/16W | A93548-043 | RES D,0402,100.00 OHM,1.00%,1/16W
[From S-01A to S-01B] To Disable JTAG ODT and Enable Onboard Terminations Rework Summary

## Slide 25
S031

## Slide 26: S031 TOP

## Slide 27: S031 BOT

## Slide 28: S031
Step 1 of 2
TOP
Action | REFDES | Description
STUFF | R2B45 | RES D,0402,100.00 OHM,1.00%,1/16W
REPLACE | R3B68 | RES D,0402,100.00 OHM,1.00%,1/16W
R3B68
R2B45

## Slide 29: S031
Step 2 of 2
BOT
Action | REFDES | Description
STUFF | R3M24 | RES D,0402,51.00 OHM,5.00%,1/16W
REPLACE | R2N7 | RES D,0402,100.00 OHM,1.00%,1/16W
R2N7

## Slide 30: NVL-S S031
Action | Item | REFDES | Current IPN | Description | New IPN | Description
STUFF | Resistor | R2B45 | N/A | N/A | A93548-043 | RES D,0402,100.00 OHM,1.00%,1/16W
REPLACE | Resistor | R3B68 | A93549-023 | RES D,0402,10.00 kOHM,5.00%,1/16W | A93548-043 | RES D,0402,100.00 OHM,1.00%,1/16W
STUFF | Resistor | R3M24 | N/A | N/A | A93549-007 | RES D,0402,51.00 OHM,5.00%,1/16W
REPLACE | Resistor | R2N7 | A93549-023 | RES D,0402,10.00 kOHM,5.00%,1/16W | A93548-043 | RES D,0402,100.00 OHM,1.00%,1/16W
[From S-01A to S-01B] To Disable JTAG ODT and Enable Onboard Terminations Rework Summary