## Slide 1: RZL-S RVP strategy
RZL RVP Architecture
RVP PDT
WW36Y2025
Rev 1.01
RZL RVP PDT sharepoint

## Slide 2
Silicon/ Package info
RVP strategy and assumptions
RZL-S package (LGA 1954) pin compatible with NVL-S
All RVP boards can fit in E-ATX chassis except S061 HSIO SKU
S011 (PnP) / S 012 (PPV) are capable of validating PL1=PL2 with VR heatsink installed.
M.2 TCSS module AIC can be supported on SKU S01x, S02x, and S041 (S031 via rework)
S051 and S061 implement JBR retimer solder-down solution
Detailed information can be found in RZL PDT Sharepoint
RZL-S/TTL-S platform to use the NVL-S RVP boards as planned
NVL-S/RZL-S RVP SKU Strategy
NVL-S/RZL-S DDR5 UDIMM 1DPC T3 4L (10L) RVP
PDG + Primary SKU (S021)
Golden BKC, PnP, Multi-Rail PSU
EV, FV, SIV, GFx, CPV, PPV
NVL-S/RZL-S DDR5 UDIMM 2DPC T3 6L (10L) RVP
PDG SKU - dTBT AIC support
Delta BKC, PnP, ATX12VO
EV, FV, SIV, GFx
NVL-S/RZL-S DDR5 UDIMM 1 DPC OC T3 6L (12L) RVP
PDG SKU – Overclocking (XMP)
Delta BKC, Partial PnP, Multi-Rail PSU
EV, FV, SIV, GFx
NVL-S/RZL-S DDR5 SODIMM 1DPC T3 6L (10L) RVP
PDG SKU – dTBT AIC support
NVL-S/RZL-S HSIO 1DPC T3 (12L) RVP
HSIO SKU
Delta BKC, PnP, ATX12VO
EV, FV, SIV, GFx
EV/FV HSIO validation
PCIe, TCSS, Multi-Rail PSU
S 031
S 041
S 051
Segment | CPU | GPU & NPU | PL1 Range | Memory | PCB Type
S | S28C S28C bLLC S52C (2x bLLC) | 32EU & NPU6 4Tile | 35-150W 125-250W | cUDIMM/cSODIMM 1DPC @8800MT/s | Type-3
 |  |  |  | UDIMM 2DPC @5600MT/s | Type-3
 |  |  |  | OC (XMP) @up to 16GT/s-G4 | Type-3
S 061
RZL-S RVP SKU Strategy
S 011
S 012
S 021
S 022
Open/Risk
New DDR5 cQDIMM (4-rank memory module) ES sample for S021 UDIMM 1DPC validation & debug underway
Notes: https://docs.intel.com/documents/Clientplatform/requirements/razor_lake_desktop_workstation/product_req_and_arch_spec.html#desktop-entry-workstation-key-feature-deltas
Griffin Cove + Golden Eagle
https://docs.intel.com/documents/ClientPlatform/srad/razor_lake_family/razor_lake_desktop/system_req_arch_doc.html
https://docs.intel.com/documents/ClientSilicon/RZL/Overview/Product.html
https://docs.intel.com/documents/ClientPlatform/domains/tcss/rzl/RZL_TCSS_PAS.html
https://docs.intel.com/documents/ClientPlatform/domains/graphics/RZL/RZL_graphics.html
https://docs.intel.com/documents/ClientPlatform/domains/sustainability/rzl/rzl_sustainability_pas.html
https://docs.intel.com/documents/ClientPlatform/domains/debug/rzl/RZL_debug_PAS.html
https://docs.intel.com/documents/ClientPlatform/domains/storage/rzl/RZL_Storage_PAS.html
https://docs.intel.com/documents/ClientPlatform/domains/telemetry/Nvl/NVL_telemetry.html

## Slide 3: RZL Desktop RVP SKU Summary
SKU Code # | Segment | RVP SKU Name | Base board SKU/ BOM SKU | RVP Base board SKU + BOM SKU | Memory Support | PCB Type | PSU | Validation Config | Type-C / Display Config | 2x7 PnP HDR | Power Accumulator Config (PAC1954)
S-011 | S | NVL-S/RZL-S DDR5 UDIMM 1DPC | Base Board SKU | S-011: NVL-S DDR5 UDIMM 1DPC EV w/ PnP HDR | cUDIMM 1DPC 8000 2R (up to 128GB) (4R cQDIMM) | Type 3 4L + 8L | Multi-rail | Full PnP HDR, PL1=PL2 w/ Validation and Debug hooks | 2x BP M.2 TCSS module 2x DP2.1 FsDP connector | Yes | PnP/System Meter(Default) *Energy Telemetry(Optional)
S-012 |  |  | BOM SKU | S-012: NVL-S DDR5 UDIMM 1DPC PPV |  |  |  | PPV (PL1=PL2) |  | No (Unstuffed) | PnP/System Meter for CPU rails only
S-021 |  |  | Base Board SKU | S-021: NVL-S DDR5 UDIMM 1DPC CRB w/o PnP HDR |  | Type 3 4L + 6L |  | Volume Runner w/o Validation and Debug hooks | 2x BP M.2 TCSS module 1x DP2.1 FsDP connector 1x HDMI2.1 connector | No (Unstuffed) | Energy Telemetry(Default) *PnP/System Meter(Optional)
S-022 |  |  | Board SKU | S-022: NVL-S DDR5 UDIMM 1DPC CPV |  |  |  | CPV |  | No (Unstuffed) | PnP/System Meter for PCH rails only
S-031 | S | NVL-S/RZL-S DDR5 UDIMM 2DPC | Base Board SKU | S-031: NVL-S DDR5 UDIMM 2DPC | cUDIMM 2DPC 5600 2R/2R (up to 256GB) | Type 3 6L + 4L | Single-rail | Delta config Full PnP HDR supported | TCP0 BP Type-C retimerless (rework to M.2 TCSS module) TCP1 Type-C with M.2 TCSS Module AIC (unstuffed by default, internal PoC) | Yes | PnP/System Meter(Default) *Energy Telemetry(Optional)
S-041 | S | NVL-S/RZL-S DDR5 SODIMM 1DPC | Base Board SKU | S-041: NVL-S DDR5 SODIMM 1DPC | cSODIMM 1DPC 8000 2R (up to 128GB) | Type 3 6L + 4L | Single-rail | Delta config Full PnP HDR supported | 2x BP M.2 TCSS module | Yes | PnP/System Meter(Default) *Energy Telemetry(Optional)
S-051 | S | NVL-S/RZL-S DDR5 UDIMM 1DPC OC | Base Board SKU | S-051: NVL-S DDR5 UDIMM 1DPC OC | cUDIMM 1DPC XMP (up to 128GB) (4R cQDIMM) | Type 3 6L + 6L | Multi-rail | Delta config, Overclocking Partial PnP HDR supported | 2 x BP JBR onboard with 80G routing | Yes, without VCCIA support | Energy Telemetry(Default) *PnP/System Meter(Optional)
S-061 | S | NVL-S/RZL-S HSIO UDIMM 1DPC | Base Board SKU | S-061: NVL-S HSIO UDIMM 1DPC | cUDIMM 1DPC (4R cQDIMM) | Type 3 4L + 8L | Multi-rail | HSIO Validation Full PnP HDR supported | 2 x BP JBR onboard with 40G routing | Yes | No support
Refer to RZL-S RVP LZ

## Slide 4: Back up

## Slide 5: RVP SKU Strategy History
WW19p3: RVP Rev0p5 – Initial SKU Strategy for RZL-S @ PC
WW45p4: RVP Rev0p7 – updated version to aligned with NVL-S RVP design update & RZL-S Silicon SKU plan
WW01p5: RVP Rev0p9 –
  Updated S-061 HSIO PCB stackup
  CCB to intercept TBT-USB4 Retimer POR simplification, HSD link - https://hsdes.intel.com/resource/15017235143
  CCB to change Front-panel Type-C solution, ZBB’d FFC implementation - https://hsdes.intel.com/resource/13012628919
WW08p5: RVP Rev0p91 –
  Updated S-031 TCSS config
  Unified NVL-S / RZL-S RVP SKU strategy
WW30p5: RVP Rev1p0 –
  Updated RVP SKU strategy to align with the NVL-S RVP implementation
WW36p4: RVP Rev1p01–
  DDR5 4R DIMM module name changed to cQDIMM from cUDIMM

## Slide 6: RZL-S Desktop RVP BOM SKU Summary
WW08Y2025
SKU Code # | Segment | RVP SKU Name | Base board SKU/ BOM SKU | RVP Base board SKU + BOM SKU (Will change with MySamples Tool SKU name later) | Memory Support (iPOR) | PCB Type | PSU | Validation Config | Type-C / Display Config | 2x7 PnP HDR | Power Accumulator Config (PAC1954)
S-011 | S | NVL-S/RZL-S DDR5 UDIMM 1DPC | Base Board SKU | S-011: NVL-S DDR5 UDIMM 1DPC EV w/ PnP HDR | UDIMM 1DPC 8800 2R (up to 128GB) | Type 3 4L + 8L | Multi-rail | Full PnP HDR, PL1=PL2 w/ Validation and Debug hooks | 2x BP TCSS M.2 module 2x DP2.1 FsDP connector | Yes | PnP/System Meter(Default) *Energy Telemetry(Optional)
S-012 |  |  | BOM SKU | S-012: NVL-S DDR5 UDIMM 1DPC PPV |  |  |  | PPV only, PL1=PL2 |  | No (Unstuffed) | PnP/System Meter for CPU rails only
S-021 |  |  | Base Board SKU | S-021: NVL-S DDR5 UDIMM 1DPC CRB w/o PnP HDR |  | Type 3 4L + 6L |  | Volume Runner EV/SI/PI w/o Validation and Debug hooks | 2x BP TCSS M.2 module 1x DP2.1 FsDP connector 1x HDMI2.1 connector | No (Unstuffed) | Energy Telemetry(Default) *PnP/System Meter(Optional)
S-022 |  |  | Board SKU | S-022: NVL-S DDR5 UDIMM 1DPC CPV |  |  |  | CPV only |  | No (Unstuffed) | PnP/System Meter for PCH rails only
S-031 | S | NVL-S/RZL-S DDR5 UDIMM 2DPC | Base Board SKU | S-031: NVL-S DDR5 UDIMM 2DPC | UDIMM 2DPC 5600 2R/2R (up to 256GB) | Type 3 6L + 4L | Single-rail | Delta config Full PnP HDR supported | 1x BP TCSS M.2 module (rework to Type-C retimerless) 1x FP Type-C with TCSS M.2 Module AIC | Yes | PnP/System Meter(Default) *Energy Telemetry(Optional)
S-041 | S | NVL-S/RZL-S DDR5 SODIMM 1DPC | Base Board SKU | S-041: NVL-S DDR5 SODIMM 1DPC | SODIMM 1DPC 8800 2R (up to 128GB) | Type 3 6L + 4L | Single-rail | Delta config Full PnP HDR supported | 2x BP TCSS M.2 module | Yes | Energy Telemetry(Default) *PnP/System Meter(Optional)
S-051 | S | NVL-S/RZL-S DDR5 UDIMM 1DPC OC | Base Board SKU | S-051: NVL-S DDR5 UDIMM 1DPC OC | UDIMM 1DPC XMP speed (up to 128GB) | Type 3 6L + 6L | Multi-rail | Delta config, Overclocking Partial PnP HDR supported | 2 x BP Rood Bridge onboard with 80G routing | Yes, without VCCIA support | PnP/System Meter(Default) *Energy Telemetry(Optional)
S-061 | S | NVL-S/RZL-S HSIO UDIMM 1DPC | Base Board SKU | S-061: NVL-S HSIO UDIMM 1DPC | UDIMM 1DPC | Type 3 4L + 8L | Multi-rail | iVE/FV HSIO Validation Full PnP HDR supported | 2 x BP Rood Bridge onboard with 40G routing | Yes | No support

## Slide 7: RZL-S RVP – Modular TCSS Configuration
Feature Support | S011 / S012 NVL S DDR5 UDIMM 1DPC | S021 / S022 NVL S DDR5 UDIMM 1DPC | S031 NVL S DDR5 UDIMM 2DPC | S041 NVL S DDR5 SODIMM 1DPC | S051 NVL S DDR5 UDIMM 1DPC OC | S061 NVL S HSIO UDIMM 1DPC
SKU Code | EV/PnP & PPV | Golden Config EV/CRB & CPV | Delta SKU | Delta SKU | Delta SKU | HSIO (PCIe bifurcation)
Pkg name: TYPEC_[0] TC1 (USB4 / HDMI2.1 / DP 2.1 ) | Back Panel TCSS Module (Default RBR module) 1) Rood Bridge w/ integrated PD, w/ EC I3C 2) June Bridge w/ discrete PD (TI PD) 3) DP 2.1 UHBR20 retimer w/ sDP connector 4) HDMI 2.1 12G retimer *80G short routing length (~85mm) /MS | Back Panel TCSS Module (Default RBR module) 1) Rood Bridge w/ integrated PD, w/ EC I3C 2) June Bridge w/ discrete PD (TI PD) 3) DP 2.1 UHBR20 retimer w/ sDP connector 4) HDMI 2.1 12G retimer *80G short routing length (~85mm) /MS | Front-Panel TCSS Module (Default RBR module) 1) Rood Bridge w/ integrated PD, w/ 10" internal Type-C cable (Feasibility WIP) * TCSS module placed at Front-panel location, >250mm routing length | Back Panel TCSS Module (Default RBR module) 1) Rood Bridge w/ integrated PD, w/ EC I3C 2) June Bridge w/ discrete PD (TI PD) 3) DP 2.1 UHBR20 retimer w/ sDP connector 4) HDMI 2.1 12G retimer *80G routing length < PDG max /MS | Back Panel Type-C Rood Bridge w/ integrated PD, soldered down w/ EC I3C TCP0/TCP1 shared SPI Flash *80G routing length @ Max loss / SL | Back Panel Type-C Rood Bridge w/ integrated PD, soldered down w/ EC I3C TCP0/TCP1 shared SPI Flash *40G routing length @ Max loss / SL
Pkg name: TYPEC_[1] TC2 (USB4 / HDMI2.1 / DP 2.1 ) | Back Panel TCSS Module (Default RBR module) 1) Rood Bridge w/ integrated PD 2) June Bridge w/ discrete PD (TI PD) 3) DP 2.1 UHBR20 retimer w/ sDP connector 4) HDMI 2.1 12G retimer *80G routing length < PDG max /MS | Back Panel TCSS Module (Default RBR module) 1) Rood Bridge w/ integrated PD 2) June Bridge w/ discrete PD (TI PD) 3) DP 2.1 UHBR20 retimer w/ sDP connector 4) HDMI 2.1 12G retimer *80G routing length < PDG max /MS | Back Panel TCSS Module (Default RBR module) 1) Rood Bridge w/ integrated PD, w/ EC I3C 2) June Bridge w/ discrete PD (TI PD) Rework option: Vertical Type-C retimerless w/ Discrete PD *80G routing length < PDG max /MS | Back Panel TCSS Module (Default RBR module) 1) Rood Bridge w/ integrated PD 2) June Bridge w/ discrete PD (TI PD) *80G routing length @ PDG max /SL | Back Panel Type-C Rood Bridge w/ integrated PD, soldered down TCP0/TCP1 shared SPI Flash *80G routing length @ PDG max / SL | Back Panel Type-C Rood Bridge w/ integrated PD, soldered down TCP0/TCP1 shared SPI Flash *40G routing length @ PDG max / SL
1x Barlow Ridge dTBT AIC | N/A | N/A | 1x dTBT Barlow Ridge AIC @PCH PCIe x4 CEM slot #2 | 1x dTBT Barlow Ridge AIC @ PCD-S PCIe x4 CEM slot #3 | N/A | N/A
 | M.2 TCSS Module Support List | M.2 TCSS Module Support List | M.2 TCSS Module Support List | M.2 TCSS Module Support List | M.2 TCSS Module Support List | M.2 TCSS Module Support List
 | 1. M.2 TCSS Module (Card 706) - Rood Bridge single retimer (5V/3A) * Rood Bridge with integrated PD 2. M.2 TCSS Module (Card 107) - June Bridge single retimer (5V/3A) * June Bridge with discrete PD (TI PD) 3. M.2 TCSS Module (Card 401) - DP2.1 retimer (enhanced sDP connector) 4. M.2 TCSS Module (Card 302) - HDMI 2.1 retimer | 1. M.2 TCSS Module (Card 706) - Rood Bridge single retimer (5V/3A) * Rood Bridge with integrated PD 2. M.2 TCSS Module (Card 107) - June Bridge single retimer (5V/3A) * June Bridge with discrete PD (TI PD) 3. M.2 TCSS Module (Card 401) - DP2.1 retimer (enhanced sDP connector) 4. M.2 TCSS Module (Card 302) - HDMI 2.1 retimer | 1. M.2 TCSS Module (Card 706) - Rood Bridge single retimer (5V/3A) * Rood Bridge with integrated PD 2. M.2 TCSS Module (Card 107) - June Bridge single retimer (5V/3A) * June Bridge with discrete PD (TI PD) | 1. M.2 TCSS Module (Card 706) - Rood Bridge single retimer (5V/3A) * Rood Bridge with integrated PD 2. M.2 TCSS Module (Card 107) - June Bridge single retimer (5V/3A) * June Bridge with discrete PD (TI PD) 3. M.2 TCSS Module (Card 401) - DP2.1 retimer (enhanced sDP connector) 4. M.2 TCSS Module (Card 302) - HDMI 2.1 retimer | N/A | N/A
NVL PDT Links:
NVL-S RVP LZ 0.91
NVL-S RVP HAS 0.9